MIPS Disassembler
User Manual

General

This is a java program which will take an input file containing instructions for the MIPS-architecture and parse them to a more readable output containing information about the instruction as well as different representations of it. To run the program an input file is required, the file needs to contain MIPS-instructions in hexadecimal or decimal representation. The output will then contain, for each instruction:

1. Line number from the input file
2. The format of the instruction
3. A decimal representation of the instruction
4. A hexadecimal representation of the instruction
5. A mnemonic representation of the instruction

The format of the instruction can be I, J or R. This represents the type of instruction and the bits are organized.

J-functions only specifies an op code (6 bits) followed by 26-bit address. These are typically jump-instructions.
I-functions specifies an op code (6 bits) followed by two registers (rs and rt) and a constant (16 bits).
R-function also specifies an op code (6 bits) followed by three registers (rs, rt and rd), a field “shamt” (shift amount, 5 bits) and a field “funct” which specifies different behavior of the instructions.

Type	Format (32 bits)
R	Opcode (6)	Rs (5)	Rt (5)	Rd (5)	Shamt (5)	Funct (6)
I	Opcode (6)	Rs (5)	Rt (5)	Immediate (16)
J	Opcode (6)	Address (26)

Note: There are exceptions to these formats depending on the opcode of the instruction.

Input a file

The file which is chosen as input to the program needs to have the following format:

0x71014802
0x8c2a0000
0xffffffff

With hexadecimal instructions starting with “0x” and ending with a newline. The file should also be stored in the same directory as the program.

Reading output

Output is displayed in the following manner:

#n I/J/R 1895909378 0x71014802 mul $t1, $t0, $at

Where n is the number of the processed instruction and I/J/R is the format of the instruction (only one is displayed). The two next columns contains decimal and hexadecimal representations of the instructions. The last column is the mnemonic representation where the first value (“mul” in this case) is the op-code of the instruction. Depending on the format of the instruction the next values varies. Values beginning with a “$” is usually registers.

Compiling and running

The source code can be found in ~oi11hkm/edu/dark/Disassembler. To compile, open the terminal and type:

javac src/*/*.java

The program is now compiled and to start the program, type:

java src/Main/Disass file.txt

Where “file.txt” is the file with MIPS-instructions to be parsed.